## Slide 1
December 18, 2012
The following pages contain histograms of packet losses for three tests: one packet per second, one packet every ten seconds, and one packet per minute.
In all tests, sensor nodes send one packet containing temperature, supply voltage, RSSI, and “pressure” which is invalid (no pressure sensor). There is no attempt to verify that the packet was received by the access point.
The nodes were arranged in various places in an office roughly 14x14 feet. During most of the measurement period nothing was moving in the space (see last page).
It’s clear from the histograms that packet rate directly affects losses. For the one second test this can be explained in part by the probability of resource conflict. For the ten second test it’s not so clear, but the results are better than the one second test.
There are ways to mitigate packet loss at the expense of power, including acknowledgments and repeater nodes. These will be explored in future tests.

## Slide 2
Chart: # of sample intervals between packets at the receiver (bin) One means no loss.
| 1 | 2 | 3 | 4 | More
1 | 10035 | 4759 | 121 | 6 | 3
2 | 6428 | 6271 | 248 | 13 | 0
5 | 6254 | 2120 | 78 | 15 | 100
8 | 14894 | 3014 | 17 | 0 | 0
9 | 7798 | 5676 | 208 | 6 | 0
10 | 8477 | 5529 | 89 | 0 | 0
13 | 7779 | 5922 | 58 | 0 | 0
14 | 10495 | 4703 | 15 | 1 | 0
Chart: # of sample intervals between packets at the receiver (bin) One means no loss.
| 1 | 2 | 3 | 4 | More
1 | 10035 | 4759 | 121 | 6 | 3
2 | 6428 | 6271 | 248 | 13 | 0
5 | 6254 | 2120 | 78 | 15 | 100
8 | 14894 | 3014 | 17 | 0 | 0
9 | 7798 | 5676 | 208 | 6 | 0
10 | 8477 | 5529 | 89 | 0 | 0
13 | 7779 | 5922 | 58 | 0 | 0
14 | 10495 | 4703 | 15 | 1 | 0
One Second Tests
Packet success rates: | node ID |  |  |  |  |  |  | 
 | 1 | 2 | 5 | 8 | 9 | 10 | 13 | 14
 | 75% | 66% | 43% | 91% | 69% | 70% | 70% | 77%
Log scale

## Slide 3
Ten Second Tests
Chart: # of sample intervals between packets at the receiver (bin) One means no loss.
| 1 | 2 | 3 | 4 | More
1 | 42923 | 112 | 2 | 1 | 0
2 | 26019 | 2981 | 220 | 110 | 198
5 | 46095 | 183 | 5 | 1 | 0
8 | 38784 | 2129 | 141 | 91 | 389
9 | 37949 | 490 | 59 | 19 | 35
10 | 36754 | 399 | 87 | 34 | 109
13 | 38895 | 13 | 0 | 0 | 0
14 | 43149 | 5 | 0 | 0 | 0
Chart: # of sample intervals between packets at the receiver (bin) One means no loss.
| 1 | 2 | 3 | 4 | More
1 | 42923 | 112 | 2 | 1 | 0
2 | 26019 | 2981 | 220 | 110 | 198
5 | 46095 | 183 | 5 | 1 | 0
8 | 38784 | 2129 | 141 | 91 | 389
9 | 37949 | 490 | 59 | 19 | 35
10 | 36754 | 399 | 87 | 34 | 109
13 | 38895 | 13 | 0 | 0 | 0
14 | 43149 | 5 | 0 | 0 | 0
Packet success rates: | node ID |  |  |  |  |  |  | 
 | 1 | 2 | 5 | 8 | 9 | 10 | 13 | 14
 | 99.8% | 78.9% | 99.6% | 81.0% | 97.7% | 93.3% | 100.0% | 100.0%
Log scale

## Slide 4
One Minute Tests
Chart: # of sample intervals between packets at the receiver (bin) One means no loss.
| 1 | 2 | 3 | 4 | More
1 | 2392 | 6 | 0 | 0 | 0
2 | 1912 | 63 | 10 | 1 | 3
5 | 2576 | 7 | 0 | 0 | 0
8 | 2827 | 13 | 1 | 0 | 0
9 | 2180 | 12 | 0 | 0 | 0
10 | 2219 | 8 | 0 | 0 | 0
13 | 2174 | 0 | 0 | 0 | 0
14 | 2403 | 0 | 0 | 0 | 0
Chart: # of sample intervals between packets at the receiver (bin) One means no loss.
| 1 | 2 | 3 | 4 | More
1 | 2392 | 6 | 0 | 0 | 0
2 | 1912 | 63 | 10 | 1 | 3
5 | 2576 | 7 | 0 | 0 | 0
8 | 2827 | 13 | 1 | 0 | 0
9 | 2180 | 12 | 0 | 0 | 0
10 | 2219 | 8 | 0 | 0 | 0
13 | 2174 | 0 | 0 | 0 | 0
14 | 2403 | 0 | 0 | 0 | 0
Packet success rates: | node ID |  |  |  |  |  |  | 
 | 1 | 2 | 5 | 8 | 9 | 10 | 13 | 14
 | 99.8% | 95.2% | 99.8% | 99.5% | 99.5% | 99.7% | 100.0% | 100.0%
Log scale

## Slide 5
14
13
10
9
8
5
2
1
AP
inside cabinet
1s: 69% 18.0
10s: 100% 17.3
1m: 100% 18.6
on top of cabinet
1s: 71% 21.6
10s: 93% 19.4
1m: 100% 22.1
on shelf
1s: 90% 21.0
10s: 81% 16.5
1m: 100% 20.4
inside cabinet
1s: 65% 18.4
10s: 79% 15.5
1m: 95% 15.6
on top of cabinet
1s: 43% 17.3
10s: 100% 19.6
1m: 100% 18.5
on desk
1s: 69% 25.4
10s: 100% 29.7
1m: 100% 26.1
on desk
on desk inside box
1s: 77% 27.0
10s: 100% 28.3
1m: 100% 27.9
on desk
1s: 75% 17.0
10s: 100% 22.0
1m: 100% 21.1
Key:
test: success_rate ave_rssi
1s, 10s, 1m: 1 second test, 10 second, 1 minute
14.5’
14.5’